## Slide 1
5 |  |  |  |  | 
4 |  |  |  |  | 
3 |  |  |  |  | 
2 |  |  |  |  | 
1 |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5
Risk Assessment Diagram
Likelihood | 
Level | Definition Levels:
1 | Not Likely
2 | Low Likelihood
3 | Likely
4 | Highly Likely
5 | Near Certainty
Consequences |  |  | 
Level | Technical | Schedule | Cost
1 | Minimal or no impact | Minimal or no impact | Minimal or no impact
2 | Minor performance Shortfall, Same approach retained | Additional activities required; able to meet key dates? | Budget increase or unit production cost<1%
3 | Moderate performance shortfall, but workarounds available | Minor schedule slip; will miss need date | Budget increase or unit production cost increase <5%
4 | Unacceptable, but workarounds available | Program critical path affected | Budget increase or unit production cost increase <10%
5 | Unacceptable, no alternatives exist | Cannot achieve key program milestone | Budget increase or unit production cost increase >10%
Likelihood
Consequence

## Slide 2: Risks
 | Risk | Likelihood | Consequences
1 | Loss of Communication | 2 | 5
2 | Collision between spacecraft | 3 | 3
3 | The spacecraft did not separate properly | 3 | 2
4 | Spacecraft unable to locate each other | 3 | 4
5 | Unable to generate enough power | 2 | 3
6 | Spacecraft separate too fast from each other | 3 | 3
7 | The spacecraft end up too far apart from each other | 3 | 4
8 | Run out of propellant before end of mission | 1 | 5
5 |  |  |  |  | 
4 |  |  |  |  | 
3 |  | 3 | 2 5 6 | 4 7 | 
2 |  |  |  |  | 1
1 |  |  |  |  | 8
 | 1 | 2 | 3 | 4 | 5
Consequence
Likelihood

## Slide 3: Risks
 | Risk | Likelihood | Consequences
9 | An error occurs during the integration of spacecraft components | 2 | 4
10 | Deorbits before six months | 1 | 5
11 | A spacecraft component fails on orbit | 1 | 3
12 | A leak develops on the propulsion unit | 1 | 3
13 | A failure occurs on the satellite during launch | 1 | 3
14 | Solar panels malfunction | 2 | 3
15 | Spacecraft components operate out of operational temperature range | 1 | 2
16 | Radiation damage | 1 | 2
5 |  |  |  |  | 
4 |  |  |  |  | 
3 |  |  |  |  | 
2 |  |  | 14 | 9 | 
1 |  | 15 16 | 11 12 13 |  | 10
 | 1 | 2 | 3 | 4 | 5
Consequence
Likelihood