## Slide 1: RCL.PL.STR1
RVM Requirement Number | STR1
RVM Requirement Wording | The total CubeSat volume shall not exceed 6U
Validation Method | Examine
Met by verifying the maximum outer dimensions of the CubeSat system fall within those dictated by a 6U architecture (20 cm x 10 cm x 300 cm) and performing a fit check with the 6U deployer.

## Slide 2: RCL.PL.STR2
RVM Requirement Number | STR2
RVM Requirement Wording | The total CubeSat mass shall not exceed 8.0 kg
Validation Method | Examine
Met by weighing the integrated spacecraft prior to launch vehicle integration.

## Slide 3: RCL.PL.STR3
RVM Requirement Number | STR3
RVM Requirement Wording | All materials used in the CubeSat shall have a Total Mass Loss of less than 1.0 %
Validation Method | Analysis
Met by only using materials found on the NASA approved list of low outgassing materials (http://outgassing.nasa.gov).

## Slide 4: RCL.PL.STR4
RVM Requirement Number | STR4
RVM Requirement Wording | All materials used in the CubeSat shall have a Collected Volatile Condensable Material of less than 0.1 %
Validation Method | Analysis
Met by only using materials found on the NASA approved list of low outgassing materials (http://outgassing.nasa.gov).

## Slide 5: RCL.PL.MOP1
RVM Requirement Number | MOP1
RVM Requirement Wording | The CubeSat must be in orbit for at least 6 months
Validation Method | Analysis
Met by constructing an accurate power budget, performing a battery charge / discharge test, performing a day-in-the-life test, performing a solar panel charge test, and performing a solar cell degradation analysis.

## Slide 6: RCL.PL.MOP2
RVM Requirement Number | MOP2
RVM Requirement Wording | The CubeSat must deorbit within 25 years of being launched
Validation Method | Analysis
Met by performing an orbital analysis using orbital parameters for various altitudes to determine orbital lifetime. If the orbital lifetime exceeds 25 years, a deorbit mechanism will be included in the design.

## Slide 7: RCL.PL.STR5
RVM Requirement Number | STR5
RVM Requirement Wording | The CubeSat system shall be conjoined prior to launch vehicle integration
Validation Method | Demo
Met by conducting an separation test then an integrated vibration test of the flight unit prior to launch vehicle integration.

## Slide 8: RCL.PL.STR6
RVM Requirement Number | STR6
RVM Requirement Wording | The CubeSat shall incorporate a Remove Before Flight pin
Validation Method | Examine
The Remove Before Flight (RBF) pin is used to cur all power to the spacecraft by physically separating the battery circuit from the rest of the spacecraft, enabling the spacecraft to be handled safely and easily while the pin is inserted.