## Slide 1
RVM Requirement Number | RCL.PLE.MOP3
RVM Requirement Wording | “The CubeSat System Shall Establish Communication between Itself and the SSRL Ground Station”
Validation Method | Analyze
The verification of successfully meeting subsequent requirements necessitates a communication link between the CubeSat system and the ground. This allows for post-maneuver verification of relative distances, roll rates, and fuel burn over the course of the mission.

## Slide 2
RVM Requirement Number | RCL.PLE.MOP4
RVM Requirement Wording | “The CubeSat System Shall Pass a Health Check Administered from the SSRL Ground Station”
Validation Method | Analyze
A health check consists of verifying that each subsystem of Jade or Turquoise has successfully survived delivery, integration, transportation, and launch before leading in to their actual missions.

## Slide 3
RVM Requirement Number | RCL.SS.MOP1
RVM Requirement Wording | “Jade and Turquoise Shall be Capable of Separating from One Another with a Relative Velocity no Greater than 5 cm/s”
Validation Method | Analyze
One of the major failure points of previous Proximity Operations missions has been the problem of initial conditions.
  If the initial relative velocity between Jade and Turquoise is too large, extremely large relative displacements can develop between each of them.
  This problem can be alleviated by reducing this initial relative velocity value such that the maximum displacement between Jade and Turquoise never goes above 100 meters.
  5 cm/s was selected based on relative orbital analyses made in MatLab for various initial relative velocities

## Slide 4
RVM Requirement Number | RCL.SS.MOP1 (Continued)
RVM Requirement Wording | “Jade and Turquoise Shall be Capable of Separating from One Another with a Relative Velocity no Greater than 5 cm/s”
Validation Method | Analyze
Relative Displacement Magnitude for 10 cm/s Initial Relative Velocity
Relative Displacement Magnitude for 50 cm/s Initial Relative Velocity

## Slide 5
RVM Requirement Number | RCL.SS.MOP2
RVM Requirement Wording | “Jade and Turquoise Shall Achieve a Local Slew Rate of Less Than 1 deg/s”
Validation Method | Analyze
Based on slew rate data obtained from previous CubeSat missions, a CubeSat with a slew rate of less than 1 deg/s can be considered to have attained stability

## Slide 6
RVM Requirement Number | RCL.SS.MOP3
RVM Requirement Wording | “Jade and Turquoise Shall Record Relative Displacement Data Between Each Other at Least Once a Second”
Validation Method | Analyze
This requirement serves as a means to verifying other requirements associated with the completion Rascal’s primary mission