## Slide 1
Rascal
Demonstration of Proximity Operations & Rendezvous in University-Class Spacecraft
Senior Team Members: Jennifer Babb, Bryant Gaume, Tom Moline, Tyler Olson, Nate Richard
Acknowledgements: Michael Swartwout Ph. D., Kyle Mitchell Ph. D.
Mission Statement
Demonstrate the performance of Rendezvous and Proximity Operations (RPO) and the inspection of a cooperating Resident Space Object (RSO) within a small spacecraft architecture.
Mission Relevance
NASA Strategic Goal 3.3: Develop and demonstrate the critical technologies that will make NASA’s exploration, science, and discovery missions more affordable and more capable.
Useful RPO Mission Data: Provide more insight into the capabilities of small spacecraft in performing RPO missions.
Launch
LV Separation and Checkout
Orient for Separation
Separation
Repeat mission without visual aids
Inspection
Stationkeep at maximum relative distance
Rendezvous
Inspection Distance Checkout
Move to maximum relative separation
Extended Ops and Deorbit
Concept of Operations
Secondary Spacecraft
Patch Rx Antenna
CDH
Microcontroller
PWR
Batteries
Regulators
Primary Aids
COM
RFID Chip
ADC
Nutation Dampening
Contact Switch
SEP
Primary Attachment
Solenoid
SSRL Ground Station
Primary Spacecraft
PRP
Thruster Block
Firing Circuit
PLD
Imager
CDH
Flash Memory
SEP
Secondary Attachment
Boeing
Power Pass
Functional Block Diagram
Mission Risks
5 |  |  |  |  | 
4 |  |  |  |  | 
3 |  |  |  |  | 
2 |  |  |  | 2, 3, 4 | 5
1 |  |  |  |  | 1
 | 1 | 2 | 3 | 4 | 5
Spacecraft unable to separate
Collision during inspection stationkeeping
Unable to rendezvous during cooperative maneuvers
Unable to rendezvous during non-cooperative maneuvers
Collision during rendezvous
Mission Information
Mission Definitions
Inspection: resolving individual components on the external surface of a resident space object.
Inspection Stationkeeping: maintaining a constant distance (<10 m) relative to a resident space object.
Remote Stationkeeping: maintaining a constant distance (>100 m) relative to a resident space object.
Rendezvous: decreasing the relative distance to a resident space object.
Architecture: Two, 3U (10 x 10 x 30cm) CubeSats (One Primary, One Secondary)
Mission Lifetime: Two Weeks for Secondary Spacecraft, 6 Months for Primary Spacecraft.
Propulsion: Cold-gas, 50 m/s of ∆V.
Imaging: 30 fps, 640x480 pixel, visual spectrum camera.
Controls: Defined through linear orbit theory and CW coordinate frame
Developed in Partnership with the Boeing Company’s Advanced Space & Intelligence Systems Organization