## Slide 1: Rascal: Small-Scale Demonstration of Proximity Operations and Rendezvous
Jennifer Babb
Bryant Gaume
Tom Moline
Tyler Olson
Nate Richard

## Slide 2
Mission Overview
Subsystem Overviews
Risk Overview

## Slide 3: Rascal Mission
Demonstrate the performance of rendezvous and proximity operations (RPO) and the inspection of a cooperating Resident Space Object (RSO) within a small spacecraft architecture.
The RPO demonstration will consist of:
  Spacecraft separation
  Stationkeeping
  Rendezvous
  Inspection
INSERT COOL RASCAL ASSEMBLY

## Slide 4: Mission Relevance
Previous RPO missions have come at a prohibitive cost.
Relates directly to NASA Strategic Goal 3.3.
Orbital Express-
300 Million Dollars
DART-
95 Million Dollars

## Slide 5: Mission Architecture
Fits within 6U CubeSat architecture (10x20x30cm).
One 3U (10x10x30cm) Primary/Interceptor Spacecraft
  Providing a 1.5U payload.
  Fits within Boeings Colony-II Bus
One 3U Secondary/Target Spacecraft
  Will have a mission lifetime of 2 weeks
  Designed to be as simple and easy to manage as possible
INSERT COOL SECONDARY SPACECRAFT ASSEMBLY

## Slide 6
Launch
LV Separation and Checkout
Orient for Separation
Separation
Repeat mission without visual aids
Inspection
Stationkeep at maximum relative distance
Rendezvous
Inspection Distance Checkout
Move to maximum relative separation
Extended Ops and Deorbit

## Slide 7: Functional Block Diagram
Secondary Spacecraft
Patch Rx Antenna
CDH
Microcontroller
PWR
Batteries
Regulators
Primary Aids
COM
RFID Chip
ADC
Nutation Dampening
Contact Switch
BRT
Primary Attachment
Solenoid
SSRL Ground Station
Primary Spacecraft
PRP
Thruster Block
Firing Circuit
PLD
Imager
CDH
Flash Memory
BRT
Secondary Attachment
Boeing
Power Pass

## Slide 8
Mission Overview
Subsystem Overviews
Risk Overview

## Slide 9: Secondary Attitude Determination and Control (ADC) Subsystem
The secondary spacecraft will utilize a nutation damping system capable of reducing slew rate to 10 ⁰/s within one orbit after separation.
INSERT COOL NUTATION DAMPING BUDGET

## Slide 10: Primary ADC Subsystem
Responsible for developing control algorithms and for all orbit planning/analysis
Control algorithms and orbit analysis are defined relative to target spacecraft within CW Coordinate Frame

## Slide 12: Delta-V Budget
Maneuver | ΔV for Each Perturbation Case (m/s) |  |  | 
 | 1 m | 5 m | 10 m | 100 m
Initial Separation | 0.5033 | 0.5134 | 0.5288 | 1.0791
ISK | 0.0067 | 0.0216 | 0.0432 | 0.4325
Continued Separation | 0.0151 | 0.0323 | 0.0538 | 0.4430
RSK | 0.0043 | 0.0216 | 0.0432 | 0.4325
Rendezvous | 0.0069 | 0.0116 | 0.0329 | 0.4220
Docking | 0.0084 | 0.0418 | 0.0837 | 0.8369
Total | 0.7903 | 1.3801 | 2.2593 | 18.3775
Margin | 98.1% | 97.2% | 95.5% | 63.2%

## Slide 13: Secondary Power Subsystem
Battery Voltage (V) | 3.6
Battery Current Rating (mA-hr) | 9000
Maximum Current Draw (mA) | 200
String Voltage (V) | 3.6
Number of Strings | 36
Total Battery Pack Current (mA-Hr) | 324000
Total Battery Pack Power (W-Hr) | 1166400
Total Orbits with LEDs On | 550.8
Total Days with LEDs On | 35.8
Secondary spacecraft has no power generation to reduce cost and complexity
Required to last a minimum of 14 days for cooperative maneuvers
Uses non-rechargeable lithium Thionyl Chloride C sized batteries for their high energy density
Largest continuous power draw comes from visual aid LEDs

## Slide 14: Propulsion Subsystem
The Rascal primary spacecraft will employ a cold-gas propulsion unit to conduct orbital maneuvers.
The propulsion subsystem provides 3-degrees-of-freedom translation capability through the use of six thruster pairs
The propulsion unit consists of two main subassemblies, the Tank Assembly and the Thruster Assembly, which are separated within the spacecraft for interface and integration purposes.
Boeing Colony-II Bus
Thruster Assembly
SLU Payload
Tank Assembly
Z+
Z-
Y+
Y-
X+
X+
X+
Y+
X-
Y-
Z+
Z-

## Slide 15: Propulsion Subsystem
Main Tank
Expansion Chamber
Control valve
Expansion Valve
Thruster Valve
Thruster Exit
Thruster Assembly
Tank Assembly

## Slide 16: Propulsion Subsystem Thruster Assembly

## Slide 17: Propulsion Subsystem Tank Assembly

## Slide 18: Communication Subsystem
The primary spacecraft will use the communications system made available on the Colony-II bus
The secondary spacecraft communication system will be developed at SLU
  Only needs to receive
  (per mission requirements)
  Consists of an RFID chip and UHF patch antenna

## Slide 19: Link Budget
 | Units | Values | Comments & References | 
Uplink Frequency | MHz | 433 | UHF Uplink | 
Station TX power | dB | 16.9897 |  | 
Gain | dBi | 15 |  | 
Ground Station Losses | dB | 3.6 | Internal Loss on the transmission lines | 
EIRP | dBW | 28.3897 |  | 
Pointing Loss | dB | 0.2 |  | 
Polarization Loss | dB | 0.2 |  | 
Atmospheric Loss | dB | 2.1 |  | 
Ionospheric Loss | dB | 0.4 |  | 
Propagation Range | km | 1500 |  | 
Path Loss | dB | 148.71 |  | 
Isotropic Signal @ S/C | dBW | -123.22 |  | 
G/T | dB-K | -21.17 |  | 
S/N0 | dBHz | 84.01 |  | 
Data Rate, B | dB | 36.02 |  | 
Eb/N0 | dB | 47.99 |  | 
Bit Rate Error |  | 0.0000 |  | 
Assumptions: 300 km circular orbit, 5° above horizon

## Slide 20: Data Budget
30 fps camera
640x480 resolution
24 bit color
16 GB of storage
Chart: 
| ISK | Transition | RSK | Margin
Data Budget | 4.1576 | 4.1576 | 2.0788 | 5.6061

## Slide 21: Structures Subsystem
Secondary spacecraft’s structure and separation system will be developed in house.

## Slide 22: Secondary Structure Mass Budget
SSRL Secondary Spacecraft |  |  |  |  |  |  |  | 
Subsystem | Item | Individual Mass (g) | Lower Bound (g) | Upper Bound (g) | Quantity | Total Lower Bound (g) | Total Upper Bound (g) | Total Mass (g)
Structures | SSRL 3U Structure (6061 T6 Aluminum) | 314 | 313 | 315 | 1 | 313 | 315 | 314
 | Threaded Rod | 11.16 | 11.07 | 11.25 | 4 | 44.28 | 45 | 44.64
 | SSRL Battery Holder | 479.0468 | 478 | 485 | 1 | 478 | 485 | 479.0468
 | Screws for 3U Structure (M3x.5mm, 6 mm long) | 1.52 | 1.512 | 1.53 | 64 | 96.768 | 97.6 | 97.28
 | Solenoid | 23.5 | 23.48 | 23.53 | 2 | 46.96 | 47.06 | 47
 | Wire Harnesses for Battery Pack to EPS | 0.68 | 0.67 | 7 | 18 | 12.06 | 126 | 12.24
 | Wire Harness for Battery Pack between batteries | 0.2 | 0.18 | 0.22 | 45 | 8.1 | 9.9 | 9
 | 6.4mm spacer (inner diameter 3.34 mm, outer 6mm) | 0.9088 | 0.896 | 0.9216 | 4 | 3.584 | 3.6864 | 3.6352
 | Solenoid Support Structures | 11.25 | 11 | 11.5 | 2 | 22 | 23 | 22.5
Communications, Power, CDH | Patch Antenna | 1.5 | 1.4 | 1.6 | 1 | 1.4 | 1.6 | 1.5
 | Energizer L91 AA Battery | 14.5 | 14.25 | 14.75 | 54 | 769.5 | 796.5 | 783
 | Custom Comm Board for EPS, CDH, COMMs (FM Receiver Module - 433 MHz, microprocessor, CDH processor) | 29.8 | 29.5 | 35 | 1 | 29.5 | 35 | 29.8
 | Additional Components | 15 | 10 | 20 | 1 | 10 | 20 | 15
Payload | Surface Mount LED lights | 0 | 0 | 0 | 20 | 0 | 0 | 0
 | PCB Boards | 80.51 | 80.46 | 80.565 | 4 | 321.84 | 322.26 | 322.04
ADC | Nutation Damping System |  |  |  |  | 0 | 0 | 0
Total |  |  |  |  |  | 2157 | 2328 | 2181

## Slide 23: Mass Budget cont’d
Remaining Mass for ADC | 
Total Allotted Mass (g) | 4000
Current Estimated Mass Used W/O ADC (g) | 2181
Total Mass Alloted for Glue and Kapton (g) | 100
Total Mass Alloted for Unforseen Circumstances (g) | 200
Mass Allotted for ADC (g) | 1519
The ADC subsystem is allotted about 1.5 kg to develop the nutation damping system that will meet mission requirements.

## Slide 24: Separation
The mission requires two independent 3U spacecrafts that integrate into a single 6U bus.
Separation of the two spacecrafts is necessary for mission success.
Testing has commenced on the effectiveness of using solenoids for the separation system.
Separation Port
Structural Support
Structural Support
Solenoid
Spring
Powering System
Interface Plate

## Slide 26
Mission Overview
Subsystem Overviews
Risk Overview

## Slide 27
Mission Risks
Spacecraft unable to separate
Collision during inspection stationkeeping
Unable to rendezvous during cooperative maneuvers
Unable to rendezvous during non-cooperative maneuvers
Collision during rendezvous
Likelihood | 1 |  |  |  |  | 
 | 2 |  |  |  |  | 
 | 3 |  |  |  |  | 
 | 4 |  |  |  | 2, 3, 4 | 5
 | 5 |  |  |  |  | 1
 |  | 1 | 2 | 3 | 4 | 5
 |  | Consequences |  |  |  | 

## Slide 28
QUESTIONS?