## Slide 1: Rascal: Small-Scale Demonstration of Proximity Operations and Rendezvous
Jennifer Babb- STR & SEP
Bryant Gaume- STR
Tom Moline- ADC
Tyler Olson- PRP & PWR
Nate Richard- COM

## Slide 2
Mission Overview
Subsystem Overviews
Risk Overview
Conclusion

## Slide 3: Rascal Mission
Demonstrate the performance of rendezvous and proximity operations (RPO) and the inspection of a cooperating Resident Space Object (RSO) within a small spacecraft architecture.
The RPO demonstration will consist of:
  Spacecraft separation
  Stationkeeping
  Rendezvous
  Inspection
CAVEAT

## Slide 4: Mission Relevance
Previous RPO missions have come at a prohibitive cost.
Relates directly to NASA Strategic Goal 3.3.
Orbital Express-
300 Million Dollars
DART-
95 Million Dollars

## Slide 5: Mission Architecture
Fits within 6U CubeSat architecture (10x20x30cm).
One 3U (10x10x30cm) Primary/Interceptor Spacecraft
  Providing a 1.5U payload.
  Fits within Boeings Colony-II Bus
One 3U Secondary/Target Spacecraft
  Will have a mission lifetime of 2 weeks
  Designed to be as simple and easy to manage as possible

## Slide 6
Launch
LV Separation and Checkout
Orient for Separation
Separation
Repeat mission without visual aids
Inspection
Stationkeep at maximum relative distance
Rendezvous
Inspection Distance Checkout
Move to maximum relative separation
Extended Ops and Deorbit

## Slide 7: Functional Block Diagram
Secondary Spacecraft
Patch Rx Antenna
CDH
Microcontroller
PWR
Batteries
Regulators
Primary Aids
COM
RFID Chip
ADC
Nutation Dampening
Contact Switch
SEP
Primary Attachment
Solenoid
SSRL Ground Station
Primary Spacecraft
PRP
Thruster Block
Firing Circuit
PLD
Imager
CDH
Flash Memory
SEP
Secondary Attachment
Boeing
Power Transfer

## Slide 8: Spacecraft Layout

## Slide 9
Mission Overview
Subsystem Overviews
Risk Overview
Conclusion

## Slide 10: Secondary Attitude Determination and Control (ADC) Subsystem
The secondary spacecraft will utilize a nutation damping system capable of reducing the slew rate
Torque Sources | Torque | 
Gravity Gradient | 5.88E-07 | Nm
Solar Radiation | 7.22E-09 | Nm
Aerodynamic | 1.09E-06 | Nm
Magnetic Dipole Requirement | 2.55 | Am2

## Slide 11: Primary ADC Subsystem
Responsible for developing control algorithms and for all orbit planning/analysis.
Control algorithms and orbit analysis are defined relative to target spacecraft within CW Coordinate Frame.

## Slide 13: Delta-V Budget
Chart: Delta-V (m/s)
| Initial Separation | Inspection Stationkeeping | Continued Separation | Remote Stationkeeping | Rendezvous | Total | Margin
1 m Pertubation | 0.5033 | 0.0067 | 0.0151 | 0.0043 | 0.0069 | 0.7903
5 m Pertubation | 0.5134 | 0.0216 | 0.0323 | 0.0216 | 0.0116 | 1.3801
10 m Pertubation | 0.5288 | 0.0432 | 0.0538 | 0.0432 | 0.0329 | 2.2593

## Slide 14: Power Subsystem
Battery Voltage (V) | 3.6
Battery Current Rating (mA-hr) | 9000
Maximum Current Draw (mA) | 200
String Voltage (V) | 3.6
Number of Strings | 36
Total Battery Pack Current (mA-Hr) | 324000
Total Battery Pack Power (W-Hr) | 1166400
Total Orbits with LEDs On | 550.8
Total Days with LEDs On | 35.8
Secondary spacecraft has no power generation to reduce cost and complexity
Required to last a minimum of 14 days for cooperative maneuvers
Uses non-rechargeable lithium Thionyl Chloride C sized batteries for their high energy density
Largest continuous power draw comes from visual aid LEDs

## Slide 15: Propulsion Subsystem
The Rascal primary spacecraft will employ a cold-gas propulsion unit to conduct orbital maneuvers.
The propulsion subsystem provides 3-degrees-of-freedom translation capability through the use of six thruster pairs
The propulsion unit consists of two main subassemblies, the Tank Assembly and the Thruster Assembly, which are separated within the spacecraft for interface and integration purposes.
Boeing Colony-II Bus
Thruster Assembly
SLU Payload
Tank Assembly
Z+
Z-
Y+
Y-
X+
X+
X+
Y+
X-
Y-
Z+
Z-

## Slide 16: Propulsion Subsystem
Main Tank
Expansion Chamber
Control valve
Expansion Valve
Thruster Valve
Thruster Exit
Thruster Assembly
Tank Assembly

## Slide 17: Communication Subsystem
The primary spacecraft will use the communications system made available on the Colony-II bus
The secondary spacecraft communication system will be developed at SLU
  Only needs to receive (per mission requirements)
  Consists of an RFID chip and UHF patch antenna

## Slide 18: Link Budget
 | Units | Values | Comments & References | 
Uplink Frequency | MHz | 433 | UHF Uplink | 
Station TX power | dB | 16.9897 |  | 
Gain | dBi | 15 |  | 
Ground Station Losses | dB | 3.6 | Internal Loss on the transmission lines | 
EIRP | dBW | 28.3897 |  | 
Pointing Loss | dB | 0.2 |  | 
Polarization Loss | dB | 0.2 |  | 
Atmospheric Loss | dB | 2.1 |  | 
Ionospheric Loss | dB | 0.4 |  | 
Propagation Range | km | 1500 |  | 
Path Loss | dB | 148.71 |  | 
Isotropic Signal @ S/C | dBW | -123.22 |  | 
G/T | dB-K | -21.17 |  | 
S/N0 | dBHz | 84.01 |  | 
Data Rate, B | dB | 36.02 |  | 
Eb/N0 | dB | 47.99 |  | 
Bit Rate Error |  | 0.0000 |  | 
Assumptions: 300 km circular orbit, 5° above horizon

## Slide 19: Data Budget
30 fps camera
640x480 resolution
24 bit color
16 GB of storage
Chart: 
| ISK | Transition | RSK | Margin
Data Budget | 4.1576 | 4.1576 | 2.0788 | 5.6061

## Slide 20: Structures Subsystem
Secondary spacecraft’s structure and separation system will be developed in house.

## Slide 21: Secondary Structure Mass Budget
Chart: 
Total Allotted Mass: 4,000 g
The ADC subsystem is allotted about 1.1 kg to develop the nutation damping system that will meet mission requirements.
Chart: 
| Structures | Com,Pwr,cdh | Payload | adc | adehesive | margin
 | 1029.342 | 829.3 | 322.04 | 1135 | 100 | 584.4

## Slide 22: Primary Structure Mass Budget
Total Allotted Mass : 3,000 g
Chart: 
| Propellant (16%) | Propulsion System (34.1%) | Vision and Navigation (5.3%) | Adhesive (3.3%) | Leftover margin (41.2%)
 | 480 | 1022.6 | 160.3 | 100 | 1237.1

## Slide 23: Separation
The mission requires two independent 3U spacecrafts that integrate into a single 6U bus.
Separation of the two spacecrafts is necessary for mission success.
Testing has commenced on the effectiveness of using solenoids for the separation system.
The Separation acceleration over a 2 second interval is 0.10057 m/s2
Separation Port
Structural Support
Structural Support
Solenoid
Spring
Powering System
Interface Plate
Magnified View

## Slide 25
Mission Overview
Subsystem Overviews
Risk Overview
Conclusion

## Slide 26
Mission Risks
Spacecraft unable to separate
Collision during inspection stationkeeping
Unable to rendezvous during cooperative maneuvers
Unable to rendezvous during non-cooperative maneuvers
Collision during rendezvous
Likelihood | 5 |  |  |  |  | 
 | 4 |  |  |  |  | 
 | 3 |  |  |  |  | 
 | 2 |  |  |  | 2, 3, 4 | 5
 | 1 |  |  |  |  | 1
 |  | 1 | 2 | 3 | 4 | 5
 |  | Consequences |  |  |  | 

## Slide 27
Mission Overview
Subsystem Overviews
Risk Overview
Conclusion

## Slide 28: Results
How has the Rascal mission changed?
Is the Rascal mission still relevant?
Is the Rascal mission still feasible?

## Slide 29
QUESTIONS?