## Slide 1
Rascal: Rendezvous and Proximity Operations
Team Bravo
Jennifer Babb
Bryant Gaume
Tom Moline
Tyler Olson
Nate Richard
First Semester Presentation
December 3, 2013

## Slide 2
Group Organization
Project Overview
Mission Success Criteria
Design Constraints
Mission Architecture
CONOPS
Risk Assessment
Schedule
Conclusion

## Slide 3: Group Organization
Group Member | Position
Jennifer Babb | 
Bryant Gaume | Structures Engineer, Propulsion Engineer
Tom Moline | Program Manager, Attitude Determination and Control Engineer
Tyler Olson | Power Engineer
Nate Richard | Communications Engineer

## Slide 4
Group Organization
Project Overview
Design Constraints
Mission Architecture
CONOPS
Risk Assessment
Schedule
Conclusion

## Slide 5: Rascal Mission Definitions
As proposed, the Rascal mission consists of a spacecraft capable of demonstrating key proximity operations.
Spacecraft proximity operations consist of orbital maneuvers made relative to a resident space object. Examples or key proximity operation terms are listed below.
Proximity operations such as these haven been tagged by NASA enabling technologies for future NASA missions.
Proximity Operation Term | Definition
Stationkeeping | Maintaining a set relative displacement between two space objects for a period of several orbits
“Escape” Maneuver | Performing an orbital maneuver that increases the relative displacement between two space objects
Rendezvous | Performing an orbital maneuver that decreases the relative displacement between two space objects within a set distance for a period of several orbits
Resident Space Object | Any satellite or space debris residing in an orbit around Earth

## Slide 6: Rascal Mission Success Criteria
In order for the Rascal mission to be considered successful, it must meet the success criteria listed below.
The Rascal mission shall demonstrate:
  Stationkeeping: performing correction maneuvers to remain within a 10-75 meter sphere of a resident space object for at least 5 orbits.
  “Escape” Maneuver: performing an orbital maneuver that intentionally increases the final displacement of the spacecraft relative to a resident space object to at least 100 meters within 1 orbit.
  Rendezvous: performing an orbital maneuver that intentionally decreases the displacement of the spacecraft relative to a resident space object to within 50 meters for at least 5 orbits.

## Slide 7
Group Organization
Project Overview
Design Constraints
Mission Architecture
CONOPS
Risk Assessment
Schedule
Conclusion

## Slide 8: Quick Note

## Slide 9: Common Spacecraft Design Constraints
Usually, the key driver of any aerospace system design is its cost and its weight.
In the case of small spacecraft design, the former plays a large role in terms of the cost associated with getting said design to orbit, while the latter place a much less significant role.
Thus, in place of weight, volume becomes a much more important constraint on any small satellite design.
  This fact is directly related to the CubeSat standard described in the previous section, which has allowed for the development of deployers for spacecraft that follow it, such as the P-POD and NLAS Deployers.
Other important design constraints include mission operation time and mission success verification.
Each of these design constraints will be discussed in detail on the following slides.

## Slide 10: Key Design Parameters: Cost
One of the greatest limits on the scope and success of any spacecraft mission is cost, specifically, the cost of getting a spacecraft to orbit.
  Launch costs alone can range from $6 million for microsatellites to $500,000 for CubeSats
However, for satellites that fall under the CubeSat category, a NASA program exists that finds and subsequently pays for launch spots for said satellites. No such program exists for microsatellites.
Beyond launch cost, the cost associated with designing, building, and testing a CubeSat (or microsatellite, for that matter) is on the order of thousands of dollars, as opposed to the millions associated with larger, more complicated spacecraft systems.

## Slide 11: Key Design Parameters: Volume
As discussed previously, another one of the largest constraints on small spacecraft design is volume.
  In the case of CubeSats, only a limited number of deployers exist.
  For each of these deployers, there exists a specific volume that a spacecraft must possess in order to be properly integrated into them.
  These volumes range from 0.0125 m3 for the Wallops 6U deployer to 0.00934 m3 for the Planetary Resources deployer.
Thus, any design, associated with meeting the Rascal mission success criteria must have the volume associated with one of these available deployers.

## Slide 12: Key Design Parameters: Mission Lifetime
Another parameter that drives small spacecraft design is the amount of time associated with executing each of the mission success criteria.
  In terms of mission operations, the longer a mission takes to run, the more likely that it is to fail before full mission success can be attained.
  Thus, it is necessary to impose a limit on the time allotted for executing any given mission, as to minimize the risk associated with prolonging the mission window, as well as to reduce the amount of resources associated with operating a given mission.
In the case of the Rascal mission, a six month mission lifetime will be imposed in order to concentrate design efforts and alleviate these risks.